## Slide 1: Ares I-X Aeroelastic and Structural Dynamics Modeling for GN&C Simulations
Eugene Heim
Ares I-X GN&C Deputy Lead
NASA Langley Research Center
Aeroservoelastics Simulation Workshop
National Institute of Aerospace
April 18-19, 2012

## Slide 2: Ares I-X
Structural dynamics major concern for Ares I
  Highest slenderness ratio of any vehicle ever flown
  First bending mode within control bandwidth
  Phase stabilization of first bending mode required
  Gain stabilization of higher modes
Ares I-X provided early flight test of first stage flight for model and modeling method validation
  Dynamically scaled at liftoff
  Dummy upper stage, Orion/LAS, and 5th segment
Made with surplus materials…
  Booster & TVC – expired Shuttle RSRM
  RoCS – disassembled from Peace Keeper ICBM
  BDM’s and BTM’s – Old Shuttle BSM motors
  Avionics – Atlas V
Primary objectives
  Demonstrate control of dynamically similar vehicle to Ares I
  Perform staging similar to Ares I
  Demonstrate assembly and recovery of new first stage element at KSC (ground ops)
  Demonstrate first stage recovery system
  Characterize internal RSRM roll torque
Flown October 28th, 2009 11:30 AM

## Slide 3: Flight Overview

## Slide 4: Aeroservoelastic Impacts on GN&C Design
Control law design required knowledge of first few bending modes
  Mode shapes influenced sensor placement and blending
  Mode frequencies influenced filter design and stabilization strategy
  Modal damping influenced effectiveness of control
Mode shapes, frequencies and even damping changed in time as fuel mass was depleted
  Required gain scheduling and scheduling of filter coefficients
  Ensure nodes and anti-nodes of phase stabilized modes do not cross sensors
Program Test Inputs (PTI’s) throughout flight
  Open loop TVC excitations and roll control blackouts
  TVC commands: 3 sets of orthogonal sum-of-signs and 1 pulse to excite structure
  Used to verify phase stabilization of first bending mode, excite aerodynamics, identify structural damping, and RSRM roll torque
Axial, torsion and higher order bending modes needed for other analysis
  Ares I thrust oscillation first discovered in early Ares I-X analysis by including axial mode and first acoustic mode of RSRM chamber
  Torsion mode allowed roll control thrusters to excite sensors leading to roll rate filter
  Clearance studies such as liftoff, staging, jettison, etc. as well as flight reconstruction require best knowledge of deformation, i.e. all the modes

## Slide 5: Sensor Locations and Mode Shapes
Similar to Ares-I design
  Baselined identical architecture Feb 2007
Major differences from Ares-I for ascent flight
  Sensor locations
  Structural dynamics
  Filter and gain coefficients
RRGU
FTINU
RRGU

## Slide 6: STARS Pitch Open Loop Gain
1st Bending Mode
4th Bending Mode
Sensor Blending Zero
Tail-Wags-Dog Zero
5th Bending Mode
3rd Bending Mode
2nd Bending Mode
6th Pitch Bending

## Slide 7: Key Points Linear Stability Analysis

## Slide 8: Baseline Nichols Charts
Linearizations from STARS
Baseline trajectory
Computed every second from 1 to 120 seconds

## Slide 9: Modal Models
Centerline
Sensor
RoCS
Nozzle
HDP
Actuator
CG
FWD RRGU 1023.8
AFT RRGU 3962.9
FTINU 1770.3
13 models representing mass conditions every 10 sec. of flight
  All modes under 25 Hz with 27 residual vectors
  Each model included 73 nodes (54 centerline, 3 sensor, 2 gimbal, 4 HDP, 2 nozzle centerline and 4 actuator attachment)
  Evaluated with RSRM pressurized “prestiffened” modes
Other models: MLP mounted model, first stage alone and upper stage alone

## Slide 10: Structural Dynamics Modeling
Standard second order flexible body EOM for each elastic mode
  Modal eigenvector and values from NASTRAN
  Damping ratio of 0.5% for all modes
Linear superposition of elastic modes onto rigid-body dynamics
Variable mass structural modeling techniques used
  Constant modes - hold one set at a time constant throughout flight
  Stepping - discrete changes from model to model
    No model formatting required
    Allows for dispersed sets of FEM models
    Care must be taken when switching models to minimize transients
  Modal interpolation - continuous piecewise linear interpolation
    No modification to modes
    Requires labor intensive modal tracking, sorting and consistent mode signs
    Some loss of orthogonality
Liftoff and staging events used least squares technique
Dispersed frequencies and mode shapes directly
  Scale factor on frequencies
  Scale factor and artificial shifts (centerline) on mode shapes

## Slide 11: Modal Interpolation
Modal selection based on Hankel-singular values (controllability and observability)
  FCS can only resolve frequencies up to 25 Hz, sensor bandwidth ~10 Hz, pitch and yaw control bandwidth ~2 Hz
  Retain at least first 3 bending mode pairs, 1st axial and 1st torsion
Modal tracking with cross-orthogonality and by hand with Patran
  Requires engineering judgment when modes combine or coalesce
Modal Decomposition
Modal Tracking and Interpolation
T=0s
T=10s
T=20s
T=30s
T=40s

## Slide 12: Modeling Dynamics on MLP
Vehicle on pad loaded by
  Gravity field
  Centripetal relief (due to Earth rotation rate)
  Winds (steady, gusts)
  Reaction from MLP
  Thermal, etc. (not modeled)
Flexible body
  Lumped masses used to load nodes due to body accelerations (gravity and centripetal relief as function of node altitude)
  Stiffness is linear, i.e. vehicle will not continue to bend due to its own weight
  Deformation at Hold Down Post (HDP) release used to initialize free-free modes
Rigid-body
  Held in place by ground reaction model until compressive loads at HDP are zero
  Structural dynamics on MLP used to initialize rigid-body EOM at HDP release

## Slide 13: Actuator Model & Structural Compliance
Shuttle heritage actuator model (Linear Simplex)
  Standalone model includes nozzle and associated compliances
  Several dispersible parameters
Structural model includes nozzle and “locked actuators”
Actuator-structural modeling “double-dipped” actuator, flex bearing and back-up structure compliance
Negligible 0 to 3 deg. shift in phase margin around first bending mode
FCS
&
Sensors
FCS - Actuator Model - Structural Model Interaction
Vehicle
Structural Dynamics
“Locked Actuator”
Nozzle Dynamics
Actuator
Structural Dynamics
Gimbaling
Nozzle Dynamics
Structural
Deformations
Actuator
Commands
Lateral Thrust,
TWD & DWT
Structural
Model
Actuator
Model
All Other Loads
Gimbal node wagon-
wheeled to nozzle
Rock Actuator
fwd
Tilt Actuator

## Slide 14: Propulsion Models
Reusable Solid Rocket Motor (RSRM)
  Submerged nozzle with flex bearing
  Chamber pressure stiffens and expands pressure vessel and compresses flex bearing causing nozzle to rotate due to kinematic coupling with actuators
  Nozzle rotation due to chamber pressure known as “deterministic error” and book kept in a separate model… possible double bookkeeping.
RSRM structural exciters
  Axial thrust applied to structural model at forward dome node
  Lateral thrust components applied at gimbal node on nozzle side of flex bearing.
  Roll torque applied to aft dome node
  Optional thrust oscillations added via generalized pressures
Roll Control System (RoCS)
  Each thruster had specific node to apply thrust
Rigid body forces transformed and translated due to structural deformation
Axial Thrust
Lateral Thrust
Roll Torque

## Slide 15: Force Following Debate
Force following transforms a force acting on the structure by the structural deformation. Creates feedback loop, input depends on output.
  Real structures with attached lateral forces will bend non-linearly
  Free-free assumed modes from NASTRAN will not
Debate between GN&C and Structural communities
  Surveyed Ares I, Shuttle, Atlas, Delta, and Aerospace Corp.
  In each case GN&C group used force following
  All but 1 structures groups recommended not to
  Should accelerations be rotated by slope or not?
Impact for Ares I-X was negligible, 0 to 5 deg. phase shift of first bending mode
Apply lateral force to model
Bending mode excited
Force following rotates applied force
Bending and axial modes excited
Simple beam example
No change in force vector
Force following

## Slide 16: Distributed Aerodynamics
Distributed line load coefficients used to simulate quasi-static aeroelastics on flexible body
  Distributed aero databases for ascent and liftoff
  Scaled to match corresponding integrated coefficients
  Local dynamic pressure, Mach, αTotal and ΦAero at each centerline node used to compute forces at node
Not applied to rigid body dynamics

## Slide 17: Aeroelastic Increments
Thrust vector increments
  Negligibly stabilizing/destabilizing depending on Mach number, nominally less than 1 deg and 1 dB on all margins
  FCS kept gimbal angles small which kept effect small
Dynamic pressure-alpha total increments
  Negligibly destabilizing, nominally less than 1 deg and 1 dB on all margins
Unsteady aerodynamics explored but not incorporated into sim
  Lots of work on reduced order model coupled with structural model
  Affects damping of structural modes: increase or decrease with dynamic pressure

## Slide 18: Summary and Conclusions
Aeroelastics negligible impact for Ares I-X
  Expected result with no significant lifting surfaces
  May be more of an issue for more flexible Ares-I
  More work needed to incorporate unsteady aero into GN&C simulations
Structural dynamics significant for Ares I-X, more so for Ares-I
  Major driver in GN&C design and analysis
  Large range in modeling techniques throughout community
  Relatively small difference in results between techniques for Ares I-X
  More work needed in modeling mass varying systems
Additional structural dynamics techniques subsequently developed for Ares-I and SLS
  Constant set of shape functions, P. Tobbe (DCI-MSFC), AIAA-2009-6023
  Least Squares Quadratic Inequality, J. Wetherbee (SAIC-MSFC)