Introduction

The IFC data set is a simulated data set based on the flight simulator “FLTz” used by the Intelligent Flight Control group at NASA ARC. Flights were preprogrammed to fly through randomly generated circular flight paths starting from San Francisco International Airport (SFO) and ending at approximately the same location. No known anomalous flights were simulated.

Data

Flights include 4 stages of flight takeoff, climb, cruise, and descent and consist of 36 parameters. There are a total of 20 flights, which range from 15 to 40 mins and are sampled at a rate of 1Hz. The flights were generated by programming in the climb/decent rate, cruise and altitude into the flight management computer and used the auto pilot to track the flight path waypoints. Approximately halfway through the flight the pilot would manual initiate the decent using the flight management computer to govern the decent rate specified.

Parameter Description

| Parameter Name | Description | Units |
| --- | --- | --- |
| timeStamp | Time Stamp | sec |
| g_exec.runtime | Run Time | sec |
| g_dyn.lat | Latitude | deg |
| g_dyn.lon | Longitude | deg |
| g_dyn.alt | Altitude | ft |
| g_sen.phi | Yaw | deg |
| g_sen.psi | Roll | deg |
| g_sen.theta | Pitch | deg |
| g_sen.ias | Indicated Airspeed | mph |
| g_sen.hdgmag | Heading Magnetic | deg |
| g_sen.ub | Velocity | ft/sec |
| g_sen.vb | Lateral Velocity | ft/sec |
| g_sen.wb | Vertical Velocity | ft/sec |
| g_sen.pb | Roll Rate | deg/s |
| g_sen.qb | Pitch Rate | deg/s |
| g_sen.rb | Yaw Rate | deg/s |
| g_aero.ubd | Forward Body-axis Acceleration | ft/sec^2 |
| g_aero.vbd | Lateral Body-axis Acceleration | ft/sec^2 |
| g_aero.wbd | Vertical Body-axis Acceleration | ft/sec^2 |
| g_aero.pbd | Body-axis Roll Acceleration | rad/sec^2 |
| g_aero.qbd | Body-axis Pitch Acceleration | rad/sec^2 |
| g_aero.rbd | Body-axis Yaw Acceleration | rad/sec^2 |
| g_act.posn[1] | Left Aileron | position (units) |
| g_eos.fail_flag[1] | Left Aileron Failure (discrete) | discrete |
| g_act.posn[2] | Right Aileron | position (units) |
| g_eos.fail_flag[2] | Right Aileron Failure (discrete) | discrete |
| g_act.posn[7] | Left Elevators | position (units) |
| g_eos.fail_flag[7] | Left Elevators Failure (discrete) | discrete |
| g_act.posn[8] | Right Elevators | position (units) |
| g_eos.fail_flag[8] | Right Elevators Failure (discrete) | discrete |
| g_act.posn[9] | Flaps | position (units) |
| g_eos.fail_flag[9] | Flaps Failure (discrete) | discrete |
| g_act.posn[13] | Rudder | position (units) |
| g_eos.fail_flag[13] | Rudder Failure (discrete) | discrete |
| g_eng.thrust[0] | Engine0 Thrust | lbs*ft/sec^2 |
| g_eng.thrust[1] | Engine1 Thrust | lbs*ft/sec^2 |