## Slide 1: Body Freedom Flutter and the X-56A
Aeroservoelastic Workshop
NASA Langley Research Center
Jeff Beranek
MAD Deputy Program Manager
John Scarcello
Research Engineering Manager
April 18-19, 2012
Create and Deliver Superior Products Through Innovative Minds

## Slide 2: Outline
Problem Statement
Body Freedom Flutter IRAD & CRAD
X-56A Program Overview
Conclusion

## Slide 3: Rigid / Flex Coupling (RFC)
Conceptual LRS
Polecat
OFW
SensorCraft
Lockheed SST
Classified II
QSST
DarkStar
SR
-
71A
Classified I
Low Tail Volume
SensorCraft
QSST
High Fineness Ratio
Rigid / Flex Coupling Is Significant In Current and Future Designs

## Slide 4: Rigid / Flex Coupling
UNSTABLE
STABLE
Rigid / Flex Coupling – Ranges from Poor Flying Qualities to BFF
BFF Shape

## Slide 5: BFF IRAD & CRAD
BFF IRAD 2005-2007
  5 Aircraft Built and Test Flown
  Verified Ability to Predict BFF Onset
  BFF04 First BFF Suppression
  BFF05 Multiple Flutter Modes Suppressed
BFF AFRL CRAD 2009
  2 Aircraft Built and Test Flown
  Included Leading Edge Stagnation Point (LESP) Sensors
  BFF06 LESP for BFF Control
  BFF07 Additional Flutter Suppression Control Development

## Slide 6: BFF IRAD & CRAD Video

## Slide 7: BFF IRAD & CRAD Summary
Vehicle | Sensor | Effector | Open Loop | Closed Loop | Notes
BFF01 | N/A | N/A | 46 | N/A | 1st Open loop
BFF02 | N/A | N/A | 46 | N/A | Verify open loop, obtain TF data
BFF03 | Pitch Rate | Outboard Flap | 44 | 47 | Missed pitch rate transport delay
BFF04 | CB Accels | Body Flap | 48 | 66 | BFF Suppression, destruction due to wing B/T flutter
BFF05 | CB & Wing Accels | Outboard Flap | 44 | 75 | BFF suppression, realized MFMC, destruction due to amplitude limit
BFF06 | LESP | Body Flap | 44 | 45 | LESP transport delay incorrectly specified
BFF07 | CB & Wing Accels | Body & Outboard Flap | 44 | 73 | Fuzzy logic MFMC successful, destruction due to amplitude limit
Demonstrated Suppression of Multiple Flutter Modes

## Slide 8: MAD Program
MAD is the Program
The Vehicle is a MUTT
X-56A is MAD
MUTT
MAD
IFAC
IFAC – Integrated Flight and Aeroelastic Controls

## Slide 9: MAD/MUTT X-56A
15.8”
27.3”
24.6”
31”
52.4”
5.5°
TOGW 480 lb
Reference Area 56.0 ft2
W/S 8.6 lb/ft2
T/W 0.225
Span 28.0 ft
Aspect Ratio 14.0
Fuselage Length 7.56 ft
Fuselage Depth 1.33 ft
Total Height 4.37 ft
Fuselage Width 3.17 ft
Wetted Area 170.70 ft2
Fuselage 41.27 ft2
Wing 113.43 ft2
Winglet 16.00 ft2
Wing Leading Edge Sweep 22.00°
Wing Trailing Edge Sweep 22.00°
Fuselage Leading Edge Sweep 60.00°
Fuselage Trailing Edge Sweep -22.00°
M.A.C. 2.00 ft
Root Chord 4.33 ft
Thickness Ratio 16.5%
Tip Chord 2.00 ft
Thickness Ratio 10.0%
Body Flap Reference Area (Ea) 1.10 ft2
Control Surface Reference Area (Ea) 1.15 ft2
Winglet Reference Area (Ea) 3. 90 ft2
Winglet Height 2.58 ft
10”
14’
19”
Wing / Body Break
Centerline to Thrust Axis
Half Span

## Slide 10: Multi-utility Aeroelastic Demonstration
Complete Research System
  2 Center Bodies
  1 Stiff Wing Set
  3 Flexible Wing Sets
  1 Ground Control Station
    With Simulation and SIL Capabilities

## Slide 11: X-56A Flex - Empty
Demonstrator Achieves Desired Flutter Behavior
Short Period
SW1B
AW1B
SW1T
AW1T
UNSTABLE
STABLE
BFF
SWBT
AWBT
Desired Flutter Band
Flex wing empty fuel flutter achieves desired speeds for minimal kinetic energy
  Body freedom flutter ~100 KEAS
  Symmetric wing bending/torsion ~119 KEAS
  Anti-symmetric wing bending/torsion ~121 KEAS
VL

## Slide 12: X-56A Flex - Full
Demonstrator Achieves Desired Flutter Behavior
Short Period
SW1B
AW1B
SW1T
AW1T
UNSTABLE
STABLE
BFF
SWBT
AWBT
VL
Desired Flutter Band
Flex wing full fuel flutter emulates full size vehicle behavior
  Body freedom flutter ~100 KEAS
  Symmetric wing bending/torsion ~121 KEAS
  Anti-symmetric wing bending/torsion ~145 KEAS

## Slide 13: X-56A Stiff - Full
Demonstrator Achieves Desired Flutter Behavior
Short Period
SW1B
AW1B
SW1T
UNSTABLE
STABLE
BFF
VL
Desired Flutter Band
Stiff wing full fuel flutter achieves > 50% flutter margin

## Slide 14: Flight Control Considerations
MUTT integrated rigid/flexible vehicle control laws will simultaneously:
  Produce desired rigid body flying qualities
  Suppress BFF and symmetric and anti-symmetric wing bending/torsion
  Reduce vehicle response due to gust to minimize loads
Integrated Rigid/Flexible Vehicle Control Essential to MAD/MUTT

## Slide 15: Stabilization Over the Entire Flight Envelope → Regulator point designs every 20 KEAS → Closed-loop poles plotted every 10 KEAS
Structural Stabilization for SM = -3, 0, 3, 6%
3 Flutter Modes Stabilized Over the Flight Envelope

## Slide 16: Zona Dynamic Flight Simulation
Goal to Achieve Real Time Simulation of Rigid/Flex Coupling
Non-Linear
6DOF Sim Model
Delta Forces
Delta Moments
Sensor Deltas
Zona DFS
  Combines non-linear 6-DOF rigid body flight dynamic model with aeroelastic model
  Simulates aeroelastic coupling between rigid body and flexible dynamics
  Implementing on MAD in real time sim

## Slide 17: X-56A

## Slide 18: Summary
BFF IRAD & CRAD
  Successful integration of flight controls and flutter disciplines
  Successful modeling of rigid/flex coupling:
    On set speed
    Mode frequencies
  Demonstrated multi-flutter mode control via multiple methods
X-56A
  Demonstrate integrated rigid body and flexible vehicle control for larger scale vehicle
  Reconfigurable for further technology demonstrations of other vehicles