## Slide 1: Stick-to-Stress Real-time Simulator (StS-RtS) Application
ASE Simulation Workshop hosted by NASA at National Institute of Aerospace
Hampton, VA Ned Lindsley, AFRL/RBS 18 Apr 2012

## Slide 2: StS-RtS Outline
What is it?
  A Physics Preserving, Real-time 6-DOF Simulation Tool for an Aeroelastic Vehicle, from Pilot Input to Global Airframe Stress
  Includes Sensors, Control Surface Freeplay and Gust
Where did it come from?
  Streamlined Stores Clearance (ZEUS, NICE Online Tools)
  Dynamic Flight Simulator (Linear, NASA Dryden SBIR & Northrop)
Why is it here?
  Generate Comprehensive Representative Dynamic Stress Histories
What else is it?
  Prototype Development, Pilot Training, CLAW Evaluation
What else can it be?
  Pilot Variation, Stores Configuration, Uncertainty Quantification

## Slide 3
Detailed Mission-Vehicle-Pilot-Specific Dynamic Stress Histories for Fatigue, DADT & Fleet Management Purposes, all via Real-time Euler-based Simulation
StS-RtS Process Overview
Detailed OML
Detailed Surface Panel Model
ZEUS Auto-Mesh
Detailed GLOBAL FEM Stress & Dynamics
MODSDF-StS
via Simulink
Detailed GLOBAL Dynamic Stress FEM
Detailed LOCAL “Breakout” Stress FEM for DADT
Crack Growth
Slice
& Dice
Modes
Cp ROMs
GAF ROMs
Stress as a BC
Seamless Fidelity Transition, Panel to Overset Euler
Full AV Stress
Real-time Surface
Pressure History
Batch or Stick Input

## Slide 4
The Streamlined Stores Clearance product consists of three sub-programs
  The Medium-Fidelity Flutter Analysis Tool (MEDFFAT) (Feb. 2005 – Dec. 2006)
  The Real-time Nonlinear Analysis System (RETINAS) (Mar. 2005 – Oct. 2007)
  The Nonlinear Interactive Clearance Environment Phase I (NICE) (Jun. 2007 – May 2009)
MEDFFAT developed an aeroelastic simulation tool to identify critical flutter/LCO cases from a massive number of fighter aircraft with store configurations.
  Outcome of MEDFFAT was the OVERCAP (replaced by ZEUS) code that integrates the essential disciplines required for aeroelastic analysis.
RETINAS provided the flight-test engineer with an off-line flowfield/aircraft visual assessment capability ready for real-time diagnostics and decision-making.
  Outcome of RETINAS is an off-line flowfield reconstruction & visualization software system.
NICE links the RETINAS tool with flight test software (Interactive Authoring Display System, IADS®, developed by Symvionics) to create an on-line capability.
  The NICE tool takes the real-time IADS data stream and provides, in near real-time, visualizations of the vehicle aeroelastic response and the unsteady flowfield.
SSC Background

## Slide 5
World’s First Process for Store Carriage Certification Based on Euler-Fidelity Screening and Real-Time Surface Pressure Reproduction in the Control Room
In-House Uncertainty Quantification Effort Underway, Full Program 2014
Streamlined Stores Clearance

## Slide 6
SSC-ZEUS, Direct Run
M=0.70, Alt=3,000 ft

## Slide 7
SSC-NICE, Sonic Bubble Vis 1
M=0.90, Alt=5,000 ft

## Slide 8: SSC-NICE, Sonic Bubble Vis 2
M=0.92, Alt=2,000 ft

## Slide 9
Combines flight dynamics and nonlinear aeroelastic models in the Simulink environment
Use ZEUS (a CFD code) to generate POD modes of the unsteady aerodynamic Cp, and generalized aerodynamic forces (GAFs)
Create Neural Net ROMs using ZEUS POD output as training data via MATLAB GUI program
NNET ROMs solved each time step in simulation to give unsteady Cp and GAFs, leading to incremental loads and control forces/moments, as well as accelerations and component loads at multiple locations
Unsteady Cp yields incremental loads history for Global Stress FEM
GAFs make rigid 6-DOF controller elastic using elastic control
Component Loads, compare to MODSDF, use in OFLCP, traditional
Predefined control inputs, or joystick for pilot-in-the-loop simulation
ΔF, ΔM
Dynamic Flight Simulator, DFS

## Slide 10
DFS

## Slide 11
Unsteady aerodynamics computed by two-layer feed-forward Neural Network model:
DFS
Input U is the aeroelastic states ηe and output y is GAF
Solve for elastic states:
Another set of Neural Net ROMs calculate the distributed Cp
Integrating the Cp gives ΔF and ΔM
Each GAF is calculated by a separate Neural Net:

## Slide 12
DFS
Structural Modes Solver
GAF ROM
Elastic Modes
Other modal forces
Component Loads
ROM modal forces
CP ROM
Δ Sensor
Incremental Sensor Calculation
H, M, α, β
Select ROMs
ΔF, ΔM

## Slide 13
Symmetric Aileron Excitation
Accelerometer Locations
Vertical Acceleration at KM507 (wing fold)
DFS

## Slide 14
Critical load/
Structure criteria
Balance
process
Design load
condition
Loads WT
tests
Mil
specs
Load aero
coeff’s
Aircraft
aero
Structural
stiffness
FEMS
Aero WT
tests
Design
team input
Past
experience
Interface
subroutines (wing,
pylon, etc)
Detailed
spec
Control
laws
Mass
properties
Propulsion
FEMS
Pressure
data
Mass
data
Criteria
MODSDF
Load
surveys
MODular Six Degree Of Freedom, MODSDF

## Slide 15: MODSDF Overview
MODSDF predicts the trajectory and attitude of a vehicle in three dimensional space
  A high fidelity, non-linear, stand-alone, simulation of vehicle motion that employs a fixed-step fourth-order Runge-Kutta integration scheme and six DOF algorithm
  Structure allows project-specific analysis requirements to be incorporated while preserving the integrity and generic quality of its embedded methods
        For example: Named pipes
Typical uses in St. Louis
    Evaluations of Flight Control System Designs
    Time-Dependent Flying Qualities and Performance Characteristics
    Flight, Store, and Ground Loads
    Weapons Separation Characteristics
    Verification of Manned Simulator Models
    Reproduction of Flight Anomalies for Incident/Accident Investigations

## Slide 16
Critical load/
Structure criteria
Balance
process
Design load
condition
Loads WT
tests
Mil
specs
Load aero
coeff’s
Aircraft
aero
Structural
stiffness
FEMS
Aero WT
tests
Design
team input
Past
experience
Interface
subroutines (wing,
pylon, etc)
Detailed
spec
Control
laws
Mass
properties
Propulsion
FEMS
Pressure
data
Mass
data
Criteria
MODSDF
Load
surveys
MODSDF-StS “Impacts”

## Slide 17
Detailed Mission-Vehicle-Pilot-Specific Dynamic Stress Histories for Fatigue, DADT & Fleet Management Purposes, all via Real-time Euler-based Simulation
StS-RtS Process Overview
Detailed OML
Detailed Surface Panel Model
ZEUS Auto-Mesh
Detailed GLOBAL FEM Stress & Dynamics
MODSDF-StS
via Simulink
Detailed GLOBAL Dynamic Stress FEM
Detailed LOCAL “Breakout” Stress FEM for DADT
Crack Growth
Slice
& Dice
Modes
Cp ROMs
GAF ROMs
Stress as a BC
Seamless Fidelity Transition, Panel to Overset Euler
Full AV Stress
Real-time Surface
Pressure History
Batch or Stick Input

## Slide 18
Detailed OML to Detailed Panel
Wing Slices in Tecplot
Detailed CFD OML
Fuselage Slices in Tecplot
Detailed Surface Panel Model

## Slide 19
Detailed Panel to ZEUS
Detailed CFD OML

## Slide 20
Global FEM to ZEUS to StS-DFS
For each Mach-Altitude “point-in- the-sky”, there is an alpha-beta ROM matrix

## Slide 21
OFLCP+d
Fatigue Data
Tracking System
Global
FEM Stress
Entire AV
Cp
GAF ROMs
ΔF, ΔM
MODSDF-StS to OFLCP & FDTS
OFLCP-QS
ON
OFF
Quasi-Steady Component Loads
Dynamic Vehicle States
Dynamic Component Loads
Dynamic Vehicle States

## Slide 22: Global to Local, Stress as BC to DADT FEM
Upper Surface
Elements – 457592 474929 474926 475716 475593 475715 458421
Upper Inboard Longeron
Canopy Flange Segment 5 (FS415-FS405)
Crack Growth

## Slide 23
Process Revision, general

## Slide 24
Side-by-Side Comparison

## Slide 25
Summary
SOA:
  Quasi-steady, empirical, stress-transfer functions (STF)
  Expensive to create, utilize and modify
  New “hot spots” only from field
    Curve-fit the curve-fit, usage severity amplification factors
MODSDF-StS:
  Dynamic, physics-based global stresses
  Component Load comparison (dynamics included)
    Quick comparison for original 16 (and re-fit) location STF
  ID global hot-spots using direct dynamic stress
  DADT FEM “cut-outs” of these global hot-spots

## Slide 26
Notes & Observations
Individual Tail Number FEMs for Detailed Stress will not Change the Modal Basis, No Need to Change MODSDF-StS
Same for Pilot Variation (Maneuver Accomplishment)
Evaluate Pilots in the Simulator for Severity
Control Law Evaluation
Uncertainty Quantification
PROTOTYPE DEVELOPMENT
Variation: Manufacture, Fuel Level, Stores, GVT Update
  Transform Cp & GAF ROMs using updated Modal Basis
  At What Level Variation must ROMs be Recalculated?
Buffet and Other Highly Separated Flows will Require a Navier Stokes Version of MODSDF-StS

## Slide 27
Pilot Variation
Flight Test Buffet Data:
AoA vs. q
Same test points, different approach to flying the maneuver, If you get this much variation in a precision oriented environment imagine the variation in the fleet

## Slide 28
Ongoing Work, F-15 C/D Fuselage
Contracting sent SOO on 04/17 for 6.3-199 add on to 6.2-211 effort
ROMs produced will also be used for Airframe Digital Twin Spiral I effort

## Slide 29
Ongoing Work, Ejection Loads, Structural Variation

## Slide 30
Ongoing Work, Ejection Loads
Marc Mignolet

## Slide 31
F-18 Inboard MK-84’s Ejection
At M = 0.727, H = 5 kft and 4.23 g Pull-Up